## Slide 1: Chapter Learning Objectives
EE3331C/EE3331E Feedback Control Systems
A/Prof. Abdullah Al Mamun, ECE, NUS
At the end of this chapter, you will be able to answer the following …
What is frequency domain method in feedback control?
What is frequency response of a linear system?
How is frequency response of a linear system related to its transfer function?

## Slide 2: Feedback System: Block Diagram
Y(s): Laplace transform of y(t), the physical variable to be controlled
Gp(s): Physical process + Actuation mechanism  Plant
Gc(s): Controller
H(s): Any dynamics involved in the feedback mechanism
N(s): Laplace transform of output disturbance or sensor noise
U(s): Laplace transform of input to the plant
Ud(s): Laplace transform of input disturbance
R(s): Laplace transform of reference signal
EE3331C/EE3331E Feedback Control Systems
A/Prof. Abdullah Al Mamun, ECE, NUS
Everything is given or known except Gc(s), which we need to design
Block diagram of a typical feedback control system

## Slide 3: Feedback System: Controller
Feedback signal
Reference
In most cases, controller is implemented as an electrical system, for example,
  An analog circuit involving Op-Amp, resistor, capacitor etc.
  A digital circuit involving a processor, DAC, ADC etc.
Controller Implemented using Op-Amp
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  Assuming that we know how to physically realize the controller, the objective in the study of feedback control system is to find the values of controller parameters, e.g., KP and KI for P+I controller
PI Controller Implemented using Op-Amp Circuit

## Slide 4: Feedback System: Controller
Controller Implemented in a Processor  Digital Implementation
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
Analog-to-Digital Converter
Digital-to-Analog Converter
previous_error = 0
integral = 0
start:
error = reference – measured_value
integral = integral + error*dt
derivative = (error – previous error)/dt
output = Kp*error + Ki*integral + Kd*derivative
previous_error = error
wait (dt)
goto start
Pseudocode of a PID controller
  Digital controller introduces delay in the feedback system
    Delay is equal to the sum of the time required by the processor to compute control signal, conversion time of ADC, and conversion time of DAC

## Slide 5: Feedback System: Things to Know
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
Study of feedback system involves
  Analysis of closed loop (CL) stability
    CL stability is what we are concerned about; open loop may be stable or unstable
  Steady-state error analysis
  Transient response analysis
  Controller design
Performance of feedback system
Laplace Transform based methods -
  Stability: Routh-Hurwitz criterion or root locus
  Steady-state error (for step, ramp etc): system type and error constant
  Transient response: rise time, overshoot, settling time etc. for step input
  Controller: three-term controller (P+I+D)
The 2nd-part of EE3331 explores the frequency-domain methods

## Slide 6: Frequency Response
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
What is frequency response?
  Steady-state response of a linear system subject to sinusoidal input
You can use Laplace Transform based method to find yss(t)
G(S)
Linear system
Next step: use partial fraction decomposition
Step 1: Take Laplace Transform of u(t) and then find Y(s)

## Slide 7: Frequency Response
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
Step 2: Partial Fraction Decomposition of Y(s)
  Note: For each individual fraction, the denominator is either a pole of G(s) or a pole of U(s)
Step 3: Take Inverse Laplace Transform of Y(s) expressed as sum of partial fractions in step 2
Poles of G(s) contribute to ytr(t) and poles of U(s) contribute to yss(t)
Zeros affect the values of k1, k2, …. etc.

## Slide 8: Frequency Response
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  For stable G(s),
So the steady-state response for sinusoidal input is,
Compare this with
Therefore,

## Slide 9: Frequency Response
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
Gain and Phase
Gain of the linear system G(s):
G(s)
Linear system
Steady-state response
Sinusoidal input
Conclusion:
  For sinusoidal input, the steady-state response of linear system is also sinusoidal
  Same frequency () at both input and output
  Input and output signals differ in amplitude and phase
Phase of the linear system G(s):
  Both gain and phase vary if frequency  is varied
  M() and () define the frequency response of a linear system

## Slide 10: Frequency Response
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
Measurement
G(s)
Linear system
To Ch1 of scope or analyzer
To Ch2 of scope or analyzer
Ch1
Ch2
  Apply Asin(it) as the input to the linear system and allow output to reach its steady-state
  Measure gain and phase for frequency i
  Repeat steps 1 and 2 for all frequencies of interest
In most frequency response analyzers, measurement is automated. Users need to specify the range of frequencies only

## Slide 11: Frequency Response
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
Relation between G(s) and its Frequency Response
  G(s): Transfer function of a linear system
  M(i): Gain of that system for frequency i rad/s
  (i): Phase of that system for frequency i rad/s
  Then,
{Refer to the Appendix 1-A for proof}
Example 1-1: Find gain and phase of the following transfer function for  = 4 rad/s
(A brief review is given in Appendix 1B on basic calculations using complex numbers)

## Slide 12: Frequency Response
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
For sinusoidal input, the steady-state output of a linear system G(s) can be found without using the Laplace transform approach
  Instead, the gain and phase of G(s) for the frequency of the input sinusoid is used
Example 1-2: Find the output signal in the steady-state of the following transfer function if the input is u(t) = 2sin(2t)
  Frequency of the input is =2 rad/s. Find gain and phase of G(s) for =2.

## Slide 13: Frequency Response
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
Frequency Response of Delay
Delay (td)
Element causing delay of td seconds
  Transfer function of the delay element,
  Frequency response,
Delay operation does not change the amplitude but the output sine wave is phase shifted by -td rad/s with respect to the input sine wave