## Slide 1: Bode Plot
It consists of two plots
  Plot of log(M) versus log 
  Plot of  versus log 
    M: gain, : phase, : frequency
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
log (M)
Degree is widely used as unit for phase
0
1
2
3
4
1
10
102
103
104
10-1
M
-1
0
45
90
-90
-45
One decade of 
One decade of 
10-1
100
101
102
103
104
Frequency is changed by factor of 10 over one decade

## Slide 2: Bode Plot
Why Log Magnitude?
  In frequency domain, controller design requires to find how the frequency response is altered if a controller is put in series with the plant
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  Overall frequency response:
  Overall gain and phase of the inter-connected system:
    Overall gain is product of individual gains
    Overall phase is sum of individual phases

## Slide 3: Bode Plot
Hand-sketching Sum of functions versus Product of functions
  Given the plots of two functions y1(x) and y2(x),
    Hand-sketching the plot of y1(x)+y2(x) is easier than sketching the plot of y1(x)y2(x)
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  Hand-sketch the plots for y1+y2 and y1y2.

## Slide 4: Bode Plot
Why Log Magnitude?
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  If Log magnitude is considered then it becomes sum
  So instead of plotting gain (or magnitude), we plot log of gain
  Given the plots of Gp(log) and Gc(log),
    It is straightforward to hand-sketch the plot of G (log)
  But it is not so simple to hand-sketch the plot of |G (log)| from the plots of |Gp (log)| and |Gc (log)|
  Sometime, magnitude axis is labeled in dB (decibel) scale

## Slide 5: Bode Plot
Sketching the Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  Point by Point sketching
  Data can be obtained either from experiment of by evaluating G(j) for  = 0, 1, 2, ….., if G(s) is given
  Direct hand-sketching if G(s) is given
  We are going to learn this technique next
Any transfer function can be expressed as product of three types of factors
[pole or zero at the origin]
[real-axis pole or zero giving linear factor]
[complex pole or zero resulting in quadratic factor]

## Slide 6: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  First, we learn to sketch the plots for each of the basic factors
  Bode plot of a composite G(s) can be sketched by adding the Bode plots of these individual factors
[one pole at the origin]
[real-axis zero]
    Bode plot of this transfer function can be sketched by adding Bode plots of the following terms
[real-axis pole]

## Slide 7: Bode Plot
Pole/zero at the origin
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  Magnitude/Gain plot:
N > 0: Integrator
N < 0: Differentiator
N = 0: Pure Gain
  With log as the independent variable, the equation above represents a straight line with slope of –N
    In Bode plot terminology, it is called –N/decade slope
  If dB scale is used,
  The slope is –20N dB/decade
  The intersection of the gain plot and the horizontal axis happens at =0 where
MdB
logM
2
1
0
-1
-2

## Slide 8: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  Slope -20N dB/decade
  Intersects the horizontal axis at 0 where
dB


## Slide 9: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  Phase is constant regardless the value of 
    Phase plot is a horizontal line with vertical axis value equal to (-N90)
  Phase plot:

## Slide 10: Bode Plot
Real-axis pole/zero (magnitude plot)
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  Real-axis Pole:
  Gain of the transfer function as function of 
    Unlike the case of integrator or differentiator, this is not a straight line’s equation
  However, the plot of log(M) or MdB versus log can be approximated by straight lines for <<a and for >>a
    Asymptotic Bode plot

## Slide 11: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
The magnitude plot of G(j) for a=10
This segment is a straight line with slope 0
This segment is a straight line with negative slope
dB

Actual magnitude plot

## Slide 12: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  Now, we find the equations of straight lines that approximate the actual plot
The approximation of magnitude plot is a horizontal straight line for  << a
  The value is same as the gain for =0 or DC-gain
Low frequency,

## Slide 13: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
Magnitude plot approximation is a straight line with slope of -20 dB/decade
High frequency,
  We can find the point of intersection of the two straight lines
  Two lines intersect at a point =c where,
This frequency is known as the corner frequency

## Slide 14: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  As we did for the real-axis pole, we are going to approximate the plot of log(M) or MdB versus log using two straight lines: one for <<b and the other for >>b
  Real-axis Zero:
Magnitude plot approximation is a horizontal straight line with vertical-axis value equal to the DC-gain,
Low frequency range,

## Slide 15: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
High frequency range,
Magnitude plot approximation is a straight line with slope of +20 dB/decade
  Two lines intersect at a point =c where,
This frequency is known as the corner frequency
log
20 dB/div

## Slide 16: Bode Plot
Sketching Bode (magnitude) Plot of Composite Transfer Function
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
  Now we know how to sketch Bode (magnitude) plot of integrator, differentiator, real-axis pole and real-axis zero.
    How do we combine them to sketch Bode plot of a composite G(s)
Bode (magnitude) plot of integrator/ differentiator/ real pole/ real zero: summary
Integrator/Differentiator | Real pole | Real zero
 | c = a | c = b
Line with -20N dB/decade slope for all  | Line with slope 0 for <c | 
 | Line with -20 dB/decade slope for >c | Line with +20 dB/decade slope for >c
Line intersects 0 dB line at 0 where (0)N = K0 | Two lines intersects at =c | 
Infinite dc-gain; can’t be shown on the plot | DC-gain is finite; vertical-axis value for the low frequency is equal to the dc-gain | 

## Slide 17: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
Example 2-1: Sketch Bode (magnitude) plot of
There is no integrator, the dc-gain is finite.
The vertical-axis value of Bode (magnitude) for frequency much smaller than the smallest corner frequency is the dc-gain
  Starting at this value for low frequency, the magnitude plot is horizontal line up to the smallest of the corner frequency, i.e., =1 where the slope is changed to -20 dB/decade
  As we move towards higher frequency, at every corner frequency the slope is changed by +20 dB/decade for a zero and -20 dB/decade for a pole

## Slide 18: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
100
101
102
103
10-1
10-2
10-3
0
10
-10
-20
-30
dB

## Slide 19: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
Example 2-2: Sketch Bode (magnitude) plot of the transfer function
The dc-gain is infinite. How to choose the leftmost point of the magnitude plot?
Option 1: Choose a frequency much smaller than the smallest of the corner frequencies of real-axis poles and real-axis zeros
  Determine the gain at that frequency. For the given G(s), let’s choose =1
  Starting at this value, draw a line with -20 dB/decade slope
  As we move towards higher frequency, at every corner frequency the slope is changed by +20 dB/decade for a zero and -20 dB/decade for a pole

## Slide 20: Bode Plot
A/Prof. Abdullah Al Mamun, ECE, NUS
EE3331C/EE3331E Feedback Control Systems
100
101
102
103
10-1
10-2
10-3
0
10
-10
-20
-30
dB